## Slide 1
Event Logging Data Flow
EP (Eprom Processor: RP2040)
EPROM Reads
Core1: Fake EPROM
Core0: Control
Emulated Memory
Inter-core FIFO
(32-bits, 8 deep)
PIO UART TX
32N1
TX FIFO 8 deep
Stream Buffer
32K Entries
16-bits each
Captured HC11 Log Write Events
(HC11 bus signals 32 bits)
Format Log Event as LogID:8/Data:8
Serial FLASH (16 MB)
EPROM Image Library
Stored as BSON docs
ECU
HC11 CPU
Log/RAM Writes
RESET
EPROM Loader
Image Combiner
Descrambler
PIO UART RX
32N1
RX FIFO 8 deep
GPS: NEO-8
UART 8N1
SD Card
GPS UART RX
8N1
RX FIFO 32 deep
WP (Wireless Processor: Pico2W)
Merge
(Atomic)
TX Ctrl
Compresses 16-bit events to 1 transfer
System Control
WP Ready
ECU Log Data Stream (2.5 Megabaud)
460800 baud
Merged
Log
Buffer
(32Kb)
Disk
Writer